## Slide 1: NVIDIA Tegra K1 系统组成及架构特点
刘寿生
2015/12

## Slide 2: 目录
TK1组成部分
TK1组成原理
TK1系统结构特点
TK1硬件和性能指标
附录
Notes: 组成部分
组成原理
系统结构特点
硬件和性能指标
附录

## Slide 3: TK1组成部分 ——概览

## Slide 4: TK1组成部分 ——处理器
处理器
  GPU
  192 CUDA核心
  Kepler 架构
  2G 显存
  326 GFLOPS
  4K 分辨率
  CPU
  4-Plus-1 四大一小核心
  ARM Cortex A15 架构
  功耗：5W
Notes: 参考：
https://developer.nvidia.com/jetson-tk1
http://elinux.org/Jetson_TK1

## Slide 5: TK1组成部分 ——内存IO
内存
  Memory 存储器
  2G 内存
  16G 外存
IO接口
  I基本接口
  USB / HDMI / LAN
  特色接口
  RS232 / SATA / Audio
  PCI-E / JTAG / GPIOs
Notes: 参考：
https://developer.nvidia.com/jetson-tk1
http://elinux.org/Jetson_TK1

## Slide 6: TK1组成部分 ——模块图
Tegra K1
SOC
USB 2.0 micro B
2 GB
DDR3
USB 3.0
A
GigE
SATA
Mini PCIe x1
HDMI
MIC In
Line Out
RTL8111GS PEX - GigE
ALC5639 Audio Codec
16 GB eMMC
SD/MMC
AS3722
PMIC
Expansion Port (DP/LVDS, Touch SPI, I2C, CSI x1, CSI x4, GPIO 6:0)
A15
A15
A15
A15
Arm7
GK20A
192 CUDA Cores
ISP
HD Video
Audio
JTAG

## Slide 7: TK1组成部分 ——实物/模块示意图

## Slide 8: TK1组成原理 ——操作系统
  Linux for Tegra (L4T)
  基于Ubuntu 14.04
  OpenGL 4.4
  VisionWorks —— ADAS辅助驾驶系统，AR增强现实，HMI人机交互，机器人
Notes: 参考：
https://developer.nvidia.com/jetson-tk1
http://elinux.org/Jetson_TK1

## Slide 9: TK1组成原理 ——并行编程平台CUDA
738 University Courses
In 62 Countries
8,000
Institutions with
CUDA Developers
2,200,000
Toolkit Downloads
506,000,000
GPUs Shipped
Notes:   395M CUDA GPUS: GPUs shipped as of 7/1/2012

## Slide 10
TK1组成原理 ——计算视觉应用开发平台VISIONWORKS
OS
SDK for CV and Image Processing
Optimized for CUDA-enabled GPUs and SOCs
Example CV pipelines with source
Open and extensible architecture
Jetson TK1 compatibility out-of-the-box
CUDA
VisionWorks

## Slide 11
TK1组成原理 —— VISIONWORKS PRIMITIVES组件
Sobel
Convolve
Bilateral Filter
Integral Image
Integral Histogram
Corner Harris
Corner FAST
Image Pyramid
Optical Flow PyrLK
Optical Flow Farneback
Warp Perspective
Hough Lines
Fast NLM Denoising
Stereo Block Matching
IME (Iterative Motion Estimation)
HOG (Histogram of Oriented Gradients)
Soft Cascade Detector
Object Tracker
TLD Object Tracker
SLAM
Path Estimator
MedianFlow Estimator

## Slide 12
Portable, open API
900+ functions
OpenCV4Tegra - Accelerated CUDA+NEON+GLSL+TBB multithreading
General Image Processing
Segmentation
Machine Learning, Detection
Image Pyramids
Transforms
Fitting
Image processing
Video, Stereo, and 3D
Camera Calibration
Features
Depth Maps
Optical Flow
Inpainting
Tracking
TK1组成原理 —— OPENCV

## Slide 13
TK1组成原理 —— 丰富的开发调试环境
Nsight Eclipse Edition IDE
NVIDIA Visual Profiler
Native compiler, debugger, profiler
CUDA-enabled libraries (cuFFT, cuBLAS, cuSparse, etc)

## Slide 14: TK1系统结构特点 ——高性能移动/嵌入式GPU
Notes: 参考：
https://developer.nvidia.com/jetson-tk1
http://elinux.org/Jetson_TK1

## Slide 15: TK1系统结构特点 ——一致化内显存（Unified Memory)
Notes: 参考：
https://developer.nvidia.com/jetson-tk1
http://elinux.org/Jetson_TK1

## Slide 16: TK1系统结构特点 ——丰富的GPU可编程API

## Slide 17: TK1系统结构特点 ——支持OpenGL4.4
OpenGL对比
OpenGL 3.0 ES
vs
OpenGL 4.x
Notes: 参考：
https://developer.nvidia.com/jetson-tk1
http://elinux.org/Jetson_TK1

## Slide 18: TK1系统结构特点 ——支持Tessellation曲面细分
Tessellation
一般嵌入式/移动处理器不支持
vs
TK1支持
Notes: 参考：
https://developer.nvidia.com/jetson-tk1
http://elinux.org/Jetson_TK1

## Slide 19: TK1性能指标 ——NVIDIA TK1 vs Apple A7
Notes: 参考：
https://developer.nvidia.com/jetson-tk1
http://elinux.org/Jetson_TK1

## Slide 20: TK1性能指标 ——NVIDIA TK1 vs Apple A7
Notes: 参考：
https://developer.nvidia.com/jetson-tk1
http://elinux.org/Jetson_TK1

## Slide 21: TK1性能指标 ——Tegra K1 vs Tegra 4
同型号对比
Tegra K1
vs
Tegra 4
Notes: 参考：
https://developer.nvidia.com/jetson-tk1
http://elinux.org/Jetson_TK1