## Slide 1: NVIDIA Tegra K1 系统生态环境与开发配置
刘寿生
2015/12

## Slide 2: 目录
TK1生态环境
远程访问TK1
CUDA安装与配置
CUDA DEMO编译测试
OpenCV安装与配置
附录
Notes: TK1简介
CUDA安装与配置
CUDA编译
CUDA-gdb调试

## Slide 3: TK1生态环境
为嵌入式量身定做
  航空电子设计
无风扇版本
  可视化，视频，数据分析
小尺寸 多接口
  2” X 2.3”，GPIO/Radar/WiFi/蓝牙
Notes: 参考：
https://developer.nvidia.com/embedded/community/ecosystem

## Slide 4: TK1生态环境
集成4块TK1
  图像处理，解密，高性能
COM Express
  326 GFLOPS，10 Watt
移动体验
  可视化，自动驾驶，车载娱乐系统

## Slide 5: 远程访问TK1
HDMI接口连接显示器或投影仪
SSH协议访问TK1
  putty
  远程登录终端Terminal
  FileZilla
  FTP上传下载文件
安装编译器
  sudo apt-get install build-essential g++
安装编辑工具
    sudo apt-get install vim
    vim使用手册见附录
Notes: 通过1根网线，台式机或笔记本与TK1实现2机互联。
之前需要一次性通过连接显示器手动设置TK1的固定IP，如192.168.1.101，以后就可以网线连接。

## Slide 6: 远程访问TK1
Putty
FileZilla
Notes: 参考：
http://soulsheng.1kapp.com/it/?p=1709

## Slide 7: CUDA安装与配置
Toolkit安装包 – TK1专用
  下载cuda-repo-l4t-r21.2-6-5-prod_6.5-34_armhf.deb
Install安装
  cd ~/Downloads
  sudo dpkg -i cuda-repo-l4t-r21.2-6-5-prod_6.5-34_armhf.deb
  sudo apt-get update
  sudo apt-get install cuda-toolkit-6-5
  sudo usermod -a -G video ubuntu
允许访问GPU
Notes: 参考网址：http://elinux.org/Jetson/Installing_CUDA
Toolkit安装包
  下载地址Download：http://developer.download.nvidia.com/compute/cuda/6_5/rel/installers/cuda-repo-l4t-r21.2-6-5-prod_6.5-34_armhf.deb
# install 安装
cd ~/Downloads
sudo dpkg -i cuda-repo-l4t-r21.2-6-5-prod_6.5-34_armhf.deb
sudo apt-get update
sudo apt-get install cuda-toolkit-6-5
sudo usermod -a -G video $USER

## Slide 8: CUDA安装与配置
添加路径到环境变量
  echo "export PATH=/usr/local/cuda/bin:$PATH" >> ~/.bashrc
  echo "export LD_LIBRARY_PATH=/usr/local/cuda/lib:$LD_LIBRARY_PATH" >> ~/.bashrc
  source ~/.bashrc
运行测试
  nvcc -V
Notes: # Add the CUDA paths
echo "export PATH=/usr/local/cuda/bin:$PATH" >> ~/.bashrc
echo "export LD_LIBRARY_PATH=/usr/local/cuda/lib:$LD_LIBRARY_PATH" >> ~/.bashrc
source ~/.bashrc
# verify
nvcc -V
Samples
# copy to home
cuda-install-samples-6.5.sh /home/ubuntu
# build
cd ~/NVIDIA_CUDA-6.5_Samples/1_Utilities
make
# run
cd deviceQuery
deviceQuery

## Slide 9: CUDA DEMO编译测试
安装DEMO
  cuda-install-samples-6.5.sh /home/ubuntu
编译DEMO
  cd ~/NVIDIA_CUDA-6.5_Samples/1_Utilities/deviceQuery
  make
  ./deviceQuery
  cd ../../5_Simulations/smokeParticles
  make
  ./smokeParticles
常用UBUNTU命令使用手册见文档末尾附录
Notes: Samples
# copy to home
cuda-install-samples-6.5.sh /home/ubuntu
# build
cd ~/NVIDIA_CUDA-6.5_Samples/1_Utilities/deviceQuery
make
# run
cd deviceQuery
deviceQuery
cd ../../5_Simulations/smokeParticles

## Slide 10: CUDA DEMO编译测试
Notes: Samples
# copy to home
cuda-install-samples-6.5.sh /home/ubuntu
# build
cd ~/NVIDIA_CUDA-6.5_Samples/1_Utilities/deviceQuery
make
# run
cd deviceQuery
deviceQuery

## Slide 11: OpenCV安装与配置
OpenCV安装包 – TK1专用
  下载 libopencv4tegra-repo_l4t-r21_2.4.10.1_armhf.deb
Install安装
  cd ~/Downloads
  sudo dpkg -i libopencv4tegra-repo_l4t-r21_2.4.10.1_armhf.deb
  sudo apt-add-repository universe
  sudo apt-get update
  sudo apt-get install libopencv4tegra libopencv4tegra-dev
OpenCV依赖库
Notes: 参考网址：http://elinux.org/Jetson/Installing_OpenCV
Toolkit安装包
  下载地址Download：http://developer.download.nvidia.com/embedded/OpenCV/L4T_21.2/libopencv4tegra-repo_l4t-r21_2.4.10.1_armhf.deb
# install 安装
cd ~/Downloads
sudo dpkg -i libopencv4tegra-repo_l4t-r21_2.4.10.1_armhf.deb
sudo apt-get update
sudo apt-get install cuda-toolkit-6-5
sudo usermod -a -G video $USER

## Slide 12: OpenCV编译测试
安装DEMO
  下载 opencv-2.4.10.tar.gz
  tar xzvf opencv-2.4.10.tar.gz
编译DEMO
  cd opencv-2.4.10/samples/cpp
  g++ edge.cpp -lopencv_core -lopencv_imgproc -lopencv_highgui -o edge
  ./edge
Notes: Samples
  下载 opencv-2.4.10.tar.gz
https://github.com/Itseez/opencv/archive/2.4.10.tar.gz
# extract
tar xzvf opencv-2.4.10.tar.gz
# build
cd opencv-2.4.10/samples/cpp
g++ edge.cpp -lopencv_core -lopencv_imgproc -lopencv_highgui -o edge
# run
./edge

## Slide 13: OpenCV编译测试
测试GPU版本的Hough直线检测算法
  g++ houghlines.cpp -lopencv_core -lopencv_imgproc -lopencv_highgui -lopencv_calib3d -lopencv_contrib -lopencv_features2d -lopencv_flann -lopencv_gpu -lopencv_legacy -lopencv_ml -lopencv_objdetect -lopencv_photo -lopencv_stitching -lopencv_superres -lopencv_video -lopencv_videostab -o houghlines
  ./houghlines ../cpp/logo_in_clutter.png
Notes: cd ../gpu
g++ houghlines.cpp -lopencv_core -lopencv_imgproc -lopencv_highgui -lopencv_calib3d -lopencv_contrib -lopencv_features2d -lopencv_flann -lopencv_gpu -lopencv_legacy -lopencv_ml -lopencv_objdetect -lopencv_photo -lopencv_stitching -lopencv_superres -lopencv_video -lopencv_videostab -o houghlines
./houghlines ../cpp/logo_in_clutter.png

## Slide 14: OpenCV编译测试
Portable, open API
900+ functions
OpenCV4Tegra - Accelerated CUDA+NEON+GLSL+TBB multithreading
General Image Processing
Segmentation
Machine Learning, Detection
Image Pyramids
Transforms
Fitting
Image processing
Video, Stereo, and 3D
Camera Calibration
Features
Depth Maps
Optical Flow
Inpainting
Tracking

## Slide 15: 附：常用UBUNTU命令使用手册
文件与文件夹
  mkdir 目录名
  创建一个目录
  rmdir 空目录名
  删除一个空目录
  rm 文件名
  删除一个文件或多个文件
  rm –rf 非空目录名
  删除一个非空目录
  touch 文件名
  创建一个空文件
  mv 重命名文件/夹
  cp 复制文件/夹
  l 列出你当前工作目录下的文件
Notes: 参考：
http://soulsheng.1kapp.com/it/?p=1709

## Slide 16: 附：常用UBUNTU命令使用手册
cd跳转/改变目录
  1.进入root目录
  输入 "cd /"
  2.进入到您自己的目录（home目录）
  输入 "cd"
  3.进入当前目录的上一层目录
  输入 "cd .."
  4.进入前一个操作的目录
  输入 "cd -"
  5.一次进入多层目录
  输入 "cd /var/www"

## Slide 17: 附：常用UBUNTU命令使用手册
Tab 自动补全单词
Ctrl + l (L) 清屏
tar 压缩/解压gz
  eg. tar czvf *.tar.gz path
  eg. tar xzvf *.tar.gz
dpkg 压缩/解压deb
  eg. dpkg -i *.deb
man 显示某命令的用法

## Slide 18: 附：vim使用手册
gedit 文件名
图形界面打开文件，远程不可用
vim 文件名
终端打开文件
  i ——进入编辑
  Esc ——退出编辑
:w ——保存
:q ——退出vim
:q! ——放弃修改退出vim
Notes: vim使用手册